## Slide 1: Computer based Optimization Technique Lecture-VI
Transportation Problem
Problem Formulation
Initial Feasible Solution
Optimal Solution

## Slide 2: Problem Formulation
There are ‘m’ number of sources and ‘n’ number of destinations
Each source ‘i’ has some available quantities (ai) and each destination ‘j’ has some requirements ‘bj’
The cell cij denotes the cost associated with transporting one unit of quantity from source ‘I’ to destination ‘j’
The problem is to minimize the total transportation cost while satisfying the requirements/ constraints
Let xij be the amount of quantities transported from source ‘i’ to destination ‘j’

## Slide 3: Mathematical Formulation
Minimize Z =

## Slide 4: Tabular Representation

## Slide 5: A few Definitions
Feasible Solution
  A set of non-negative individual allocations (xij >= 0) which simultaneously removes deficiencies/ satisfies constraints is called a feasible solution
Basic Feasible Solution
  A feasible solution to a m-origin, n-destination problem is said to be basic if the number of positive allocations are m+n-1. Otherwise it is known ‘degenerate BFS’
Optimal Solution
  A feasible solution is said to be optimal if it minimizes the total transportation cost

## Slide 6: Steps to find optimal solution
Methods to find the Initial Basic Feasible Solution
  North-West Corner Rule
  Lowest Cost Entry (Matrix Minimum) Method
  Vogel’s Approximation (Unit cost Penalty) Method
To find optimal solution by successive improvements in the initial basic feasible solution

## Slide 7: North-West Corner Rule
Start with cell (1,1) i.e the north west corner
Allocate as much as possible [minimum (a1,b1)]
Move to the right or down depending on the remaining non-zero value in availability or requirements
Continue from left to right and top to bottom

## Slide 8: North-West Corner Rule - Example
Total Transportation Cost = 19*5 + 30*2 + 30*6 + 40*3 + 70*4 + 20*14 = 1015
Factory/Warehouse | W1 | W2 | W3 | W4 | Available
F1 | 5 | (30) 2 | (50) 0 | (10) 0 | 7
F2 | (70) 0 | (30) 6 | (40) 3 | (60) 0 | 9
F3 | 0 | (8) 0 | (70) 4 | (20) 14 | 18
Requirements | 5 | 8 | 7 | 14 | 34

## Slide 9: Algorithmic Summary of North-West Corner
Step-1: First Assign in the cell occupying the upper-left (north-west corner) with the maximum possible value i.e min(a1,b1)
Step-2:
  If b1>a1, move vertically downwards to second row and make the second allocation of x21 = min (a1, b1-x11)
  If b1<a1, move horizontally right to the second row and make allocation x21 = Min(a1-x11,b2)
  If there is a tie (a1 = b1), move diagonally down

## Slide 10: Lowest Cost Entry Method
Start with the lowest cost entry. In this example it is 8 in cell (3,2) and allocate as much as possible [minimum of ai and bj]
  Allocate 8 to cell (3,2) as minimum of (8,18) is 8
  The requirement of warehouse-2 is fulfilled and no other allocation can be made in that column
Continue this process by ignoring the rows/ cols where the allocation is made until all requirements are satisfied

## Slide 11: Example and Demonstration
Factory/Warehouse | W1 | W2 | W3 | W4 | Available
F1 | 0 | (30) 0 | (50) 0 | (10) 7 | 7
F2 | (70) 2 | 0 | 7 | (60) 0 | 9
F3 | 3 | (8) 8 | 0 | (20) 7 | 18
Requirements | 5 | 8 | 7 | 14 | 34
Transportation Cost = 2*70 + 3*40 + 8*8 + 7*40 + 7*10 + 7*20 = 814

## Slide 12: Algorithmic summary of Lowest cost entry method
Srep-1: Determine the smallest cost of the cost matrix and let it be cij. Allocate Xij = Min(ai, bj)
Step-2:
  If xij = ai, strike out the ith row and update bj = bj – ai, goto step3
  If xij = bj, strike out the jth col and update ai = ai-bj, goto step 3
  If xij = ai = bj, strikeout either ai or bj but not both
Step-3: Repeat step 1 and 2 until all allocations are made

## Slide 13: Vogel’s Approximation Example
Step-1: Construct the cost and requirement table
Step-2: Append one row and one column and put the difference the lowest and second lowest cost entry of the corresponding row and col. This is also know as penalty
Step-3: Select the row with largest penalty. If a tie, choose any one.
Step-4: Allocate maximum to the cell with lowest cost corresponding to the chosen row/col
Step-5: Strike out the row/col for which allocation have been made
Step-6: Update the table after changing the requirements
Step-7: Repeat steps thru 3-6 until all allocations are made

## Slide 14: Example and Demonstration
Fact/Ware | W1 | W2 | W3 | W4 | Avail | Penalty
F1 | 19 | 30 | 50 | 10 | 7 | 9
F2 | 70 | 30 | 40 | 60 | 9 | 10
F3 | 40 | 8 | 70 | 20 | 18 | 12
Req | 5 | 8 | 7 | 14 |  | 
Penalty | 21 | 22 | 10 | 10 |  | 

## Slide 15: Example and Demonstration
Fact/Ware | W1 | W3 | W4 | Avail | Penalty
F1 | 19 | 50 | 10 | 7 | 9
F2 | 70 | 40 | 60 | 9 | 20
F3 | 40 | 70 | 20 | 10 | 20
Req | 5 | 7 | 14 |  | 
Penalty | 21 | 10 | 10 |  | 

## Slide 16: Example and Demonstration
Fact/Ware | W3 | W4 | Avail | Penalty
F1 | 50 | 10 | 2 | 40
F2 | 40 | 60 | 9 | 20
F3 | 70 | 20 | 10 | 50
Req | 7 | 14 |  | 
Penalty | 10 | 10 |  | 

## Slide 17: Example and Demonstration
Fact/Ware | W3 | W4 | Avail | Penalty
F1 | 50 | 10 | 2 | 40
F2 | 40 | 60 | 9 | 20
Req | 7 | 4 |  | 
Penalty | 10 | 50 |  | 

## Slide 18: Example and Demonstration
Fact/Ware | W3 | W4 | Avail | Penalty
F2 | 40 | 60 | 9 | 20
Req | 7 | 2 |  | 
Penalty | 40 | 60 |  | 

## Slide 19: Example and Demonstration
Fact/Ware | W3 | Avail | Penalty
F2 | 40 | 7 | 20
Req | 7 |  | 
Penalty | 40 |  | 

## Slide 20: Example and Demonstration
Fact/Ware | W1 | W2 | W3 | W4 | Avail | 
F1 | (19) 5 | 30 -- | 50 -- | 2 | 7 | 
F2 | 70 -- | 30 -- | (40) 7 | (60) 2 | 9 | 
F3 | 40 -- | (8) 8 | 70 -- | (20) 10 | 18 | 
Req | 5 | 8 | 7 | 14 |  | 
Total Transportation Cost = 779